## Slide 1
GOYO
Taerim Kim, Information System
Wongyu Lee, Information System
Junill Jang, Information System
Hoyoung Chung, Information System
Connecting you to
better focus

## Slide 2
Motivation
  Work from Home: New Normal
Widespread adoption of working/studying from home post-COVID
  Reduced Concentration from Appliance Noise
Continuous operating sounds (e.g., fans) hinder work immersion
Wearing ANC-enabled devices
ANC(Active Noise Cancellation): Cancels external noise by generating opposing sound waves simultaneously

## Slide 3
Motivation
  Work from Home: New Normal
Widespread adoption of working/studying from home post-COVID
  Reduced Concentration from Appliance Noise
Continuous operating sounds (e.g., fans) hinder work immersion.
Wearing ANC-enabled devices
ANC(Active Noise Cancellation): Cancels external noise by generating opposing sound waves simultaneously

## Slide 4
Our Project
Non-wearable Spatial Control
Creates a 'Quiet Zone' using only speakers
without wearing any devices.
Selective Cancellation
Eliminates only target noise (e.g., appliances) while preserving essential sounds.
Our project “GOYO”
Current ANC
Device Dependency
Requires wearing earphones/headset Ear pressure and physical pain
Indiscriminate Blocking
Blocks all sound
including alarms, conversation

## Slide 5
Demo Video

## Slide 6
System Architecture

## Slide 7
Technical features
Detection & Collection
Batch-based Verification
  Real-time Decibel Detection (VAD State Machine)
  Collects buffered data with overlapping intervals
  using Sliding Window method
Generates control signals only upon >80% match
within a 3-second buffer
Minimizes the risk of misclassification

## Slide 8
Dataset & training
Used open source data
UrbanSound8K, ESC-50, Freesound API Target (40~60 for each class)
Refridgeator, Vacuum Cleaner, AC
Microwave, Hair Dryer
Non-Target (190)
Daily Life Noise (e.g. Conversation)
Total 480+ audio data set
Dataset
Data Preprocessing
Resampled all audio to 16kHz and removed silent intervals
Data Augmentation
Noise Injection & Pitch Shifting
To address low diversity by insufficient Target data
Relatively higher augmentation probability to Target class
Preprocessing & Argumentation

## Slide 9
Dataset & training
Base Model: YAMNet
Audio classification model based on MobileNet, optimized for mobile and edge environments
2-Phase Fine-tuning
Phase 1 : Backbone Freeze
Phase 2 : Backbone Unfreeze & Low Learning Rate
Parameter
Epoch: 100 Batch size: 16
Model Training

## Slide 10
Backbone Model
Accuracy
(%)
Model Size
(MB)
Inference speed
(ms)
Parameters
(Million)
YAMNet
PANNs
3.05
4.02
81.3
34
215
84.2
63.5
311.2
Accuracy
Outperformed PANNs +20.7%p
Low Latency
6x faster inference speed
Lightweight architecture
Optimized for storage-constrained edge devices

## Slide 11
Model Compression
Before
(server/pc)
After
(Raspberry Pi)
Format
Inference Speed
Size
TensorFlow
TFLite
.keras
.tflite
480MB
1MB
2.5sec
< 0.1sec

## Slide 12
Noise
Anti-noise
How ANC Works

## Slide 13
Spatial ANC
Reference Mic
Error Mic
User
Anti-noise Speaker
ANC
Module
Feedback
Filtered
Anti-noise
Appliance
Reference
Noise

## Slide 14
2nd path
User
Anti-noise Speaker
Target Noise
Anti-noise
Sound modified
By physical environment

## Slide 15
2nd path
User
Anti-noise Speaker
Target Noise
Anti-noise
Sound modified
By physical environment

## Slide 16
ANC Metrics

## Slide 17
Conclusion
  Spatial ANC
  Target noise classification
  Real-time responsiveness
  Hardware dependency
  High latency sensitivity
1
2
3
Achievement
Limitations
Future Improvement
  Enhanced ANC algorithms
  -RL adaptive ANC
  -Time series analysis ANC

## Slide 18
Thank You
github | https://github.com/SWE-ITE/GOYO
youtube | ~~
notion | ~~~~~
Visit Link